## Slide 1
Design of an autonomous energy management agent
for a hybrid microgrid
Prepared by: Julian Banks (BNKJUL001)
Prepared for: Professor Sunetra Chowdhury

## Slide 2: Overview
1
3
5
6
4
2
Load forecasting
Results & agent’s behavior
Hybrid Microgrid
RL environment
Review
Conclusion & wrapping up

## Slide 3: Review
Autonomy
Energy management systems
(EMS)
Hybrid microgrids
Sheduling
AC and DC load
Suite DC nature of renewables
Serve growing DC demand
Scheduling of energy
Machine learning (ML) forecasts
Reinforcement Learning (RL)
Simulate complex environments
Train autonomous agents

## Slide 4: The plan
Hybrid Microgrid
ML-generated forecasting
RL-trained autonomous EMS
Reduced energy costs!

## Slide 5
Hybrid microgrid parameters
AC load data
UCT building
DC load data
Simulated

## Slide 6
Load forecasting
AC mean-per-step MAPE
16.82%
DC mean-per-step MAPE
23.47%
Evaluated models
LSTM
SARIMA
Neural net

## Slide 7
RL environment

## Slide 8
Action space
Purchase requested energy
Charge battery with excess
Draw shortfall from battery
Purchase any remaining shortfall
Purchase request
0 – 300 kWh
Reward structure

## Slide 9
Observation space
24 step ahead forecasts
Power balance
Time of use tariff schedule
Load shedding schedule
Current
Power balance
Battery level
Time of use tariff
Load shedding

## Slide 10
Agent’s
behaviour
Power balance
Battery level
Energy purchases
Peak
Standard
Off-peak
Agent
Baseline

## Slide 11
Results
Stable grid
5.38% reduced energy costs
Un-stable grid
6.12% reduced energy costs
98.6% decrease in diesel generation
100% decrease in unmet demand

## Slide 12: Conclusion
EMS agent
Saved R52 895 in stable grid conditions
Saved R62 664 in unstable grid conditions
Eliminated unmet demand
Reduced diesel generation
Hybrid microgrid
Load forecasts
16.82% - AC load
23.47% - DC load
Sufficiently accurate for EMS
Suitable for RL modeling
Able to meet loads
Economically feasible

## Slide 13: Future work
Generation forecasts
ML-generated energy production
Weather API’s
RL Training
Explore different algorithms
Tune hyperparameters
Real-world integration
Test feasibility of SCADA integration

## Slide 14: Thanks
Special thanks to my supervisor, UCT, and everyone who supported me along the way.